## Slide 1: Modular Robot Time Protocol (MRTP)
Univ. of Franche-Comté / IUT-BM
Jury de soutenance:
Abdallah Makhoul
Montbéliard 2020
Bogdan Gorelkin
Hassan Hijazi
Time synchronization for programmable matter based modular robots

## Slide 2: Modular Robot Time Protocol (MRTP) - a network-wide time synchronization protocol for modular robots.
1
* protocol reviewed on Blinky Blocks hardware
The maximum number of blink blocks in the network that can be controlled- 27 775
Protocol is able to keep a Blinky Blocks system synchronized to a few milliseconds, using few network resources at runtime, even-though the Blinky Blocks hardware clocks exhibit very poor accuracy and resolution
✓
✓
* the Blinky Blocks are equipped with a very low accuracy (10,000 parts per million (ppm)) and poor resolution (1 millisecond) clocks

## Slide 3: a common notion of time…
2
Distributed time synchronization is necessary to keep each modules local clock synchronized to a global timescale
Network-wide time synchronization protocols aim to keep a small offset between local clocks and a global reference time
is the coordination of events to operate a system in unison
Every module has its own notion of time provided by its own hardware clock

## Slide 4: Why Modular Robot Time Protocol (MRTP) is better?
3
  central time master election
protocol achieves its performance by combining several mechanisms:
  fast and recursive propagation of synchronization waves along the edges of a breadth-first spanning tree
  low-level timestamping with per-hop compensation for communication delays using the most-appropriate method for the target platform
  clock skew compensation using linear regression
* Linear regression - is a linear approach to modeling the relationship between a scalar response (or dependent variable) and one or more explanatory variables (or independent variables)

## Slide 5: MRTP algorithm
4
begin MRTP
select center
(example ABC-Center)
do we have a new modules?
yes
no
root as central module master of time
Each module should send the BACK message to his parents*
*At each hop, the transmitted time is updated to take into account communication delays and time of residence in intermediate modules
The time master sets the global timescale as YTM

## Slide 6: Periodic Synchronization
5
Y = a * x + b
At each hop, the transmitted time is updated to take into account communication delays and time of residence in intermediate modules. Slave modules use a linear model to compensate for clock skew.
the central sends a sync message to its children each parent module, starting from
Calculate new Gt using linear equation
Synchronization points for the linear regression are made
begin MRTP

## Slide 7: How does it work on schematic
6
time master

## Slide 8: Implementation of algorithm on VisibleSim
7
  Build the spanning tree
MRTP
  Get BACK_MSG
  Broadcast a sync message
  Initialize time
Tasks to achieve the goal
  Periodic Synchronization
  Compute linear regression
Inculcation of Simple Algorithm for Improving Time Synchronization in Wireless Sensor Networks

## Slide 9: Spanning tree
8

## Slide 10: Go message
9

## Slide 11
Summary:
Parent sends GO_MESSAGES to his children
Each children starting from the leafs sends BACK_MESSAGES containing the estimated local time
Each parent wait the Back Message from all his children's and then sent his own back message to his parents (its mean his own local time)
Back message
10

## Slide 12: Global Clock Initialization
maximum time
as a master
time
Leader
Leaf 1
Leaf 2
Leaf 3
GO MSG
GO MSG
GO MSG
3
3
2
3
2
1
We check the local time of each module and assign time of the module with a greater time as a time master
Leaf 1
11

## Slide 13: Sync message
Summary:
After the master received last back message:
It will start to broadcast sync message to the tree
The sync message contains the time estimate of the “master time”
This message will be periodically sent.
For what???
12

## Slide 14: Why do synchronizations matter?
13
  Unsynchronized
  Unsynchronized
  Unsynchronized

## Slide 15: Simple Algorithm for Improving Time Synchronization in Wireless Sensor Networks
14
According to a scientific publication (2), this algorithm allows you to speed up synchronization by 4-5 times. This is achieved by using the formulas:

## Slide 16: Analysis of the obtained results
15
  configTree.xml
  configCube.xml
Seed Block_ID = 1
Seed Block_ID = 1
The experiment was carried out on several models.
  to get result we were using follow command:
  ./[name of project] –c [config file xml] >resultat.txt

## Slide 17: Comparison of sync speed for [configTree.xml] model
15
MRTP without improving
MRTP with improving
Chart: configTree.xml MRTP improved
 | 148892 | 96681 | 71096 | 55544 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: configTree.xml MRTP not improved
 | 425945 | 485399 | 533890 | 601558 | 601107 | 448149 | 189046 | 1 | 0 | 1 | 6644 | 27847 | 81157 | 140318 | 130333 | 62651 | 3300 | 464 | 2

## Slide 18: Comparison of sync speed for [configCube.xml] model
15
MRTP without improving
MRTP with improving
Chart: configCube.xml MRTP improved
 | 127248 | 82729 | 60750 | 47305 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: configCube.xml MRTP not improved
 | 440178 | 620013 | 777740 | 898869 | 775775 | 614076 | 348609 | 0 | 0 | 0 | 6348 | 45133 | 105150 | 192391 | 236887 | 154894 | 25682 | 3903 | 2771 | 3299 | 4086 | 11447 | 5421

## Slide 19: Conclusions
  Entering the infinity loop for
Challenges during implementation
  Sending the time was always giving "0"
  Implementation of Linear regression using time
  No documentation
  Sending the local time of the Master_Time periodically
Upcoming work
  implantation of Simple algorithm for improving time synchronisation in wireless sensor networks
  implement this algorithm on BlinkyBlocks to check it in real
16
The combination of the two algorithms allows you to speed up the synchronization algorithm, which is certainly important when working with a sufficiently large number of modules.

## Slide 20: Sources:
Naz, A., Piranda, B., Goldstein, S. C., & Bourgeois, J. (2016, February). A time synchronization protocol for modular robots. In Parallel, Distributed, and Network-Based Processing (PDP), 2016 24th Euromicro International Conference on (pp. 109-118). IEEE.
OMNI Team (FEMTO-ST/DISC/OMNI)
https://www.youtube.com/channel/UCUFwQq2i-s_gFhTJ0l2-PBQ
Programmable matter
https://projects.femto-st.fr/programmable-matter/synchronization
17
Gao Q., Blow K. J., Holding D. J. Simple algorithm for improving time synchronisation in wireless sensor networks //Electronics Letters. – 2004. – Т. 40. – №. 14. – С. 889-891.